## Slide 1: Project Presentation
Ehsan

## Slide 2: Review: Cheetah Video

## Slide 3: Review: Takeaway message
A generalizable learning methodology needs to be integrated in such robots!

## Slide 4: Project Proposal
Project Description:
  Simulating a 1-legged robot, and controlling it using RL.
Simulation Details:
  Simulation Physics Engine: Bullet
  API : PyBullet
Implementation:
  Algorithm: PPO
Target:
  avoiding a moving obstacle on a conveyer belt

## Slide 5: Challenges
The first challenge was to set up the simulator properly.
  Setting the friction coefficients properly was a challenge.
  Motors should be deactivated and then used properly.
  Robot description should be very precise.
  …

## Slide 6: Challenges
Reward shaping was also an important challenge.
  The potential energy is the first shot
    However, it is unstable.
  The motor energy consumption could help in stabilization
    However, the robot could lean on itself for avoiding energy consumption.
  Self and ground collision costs could help.
  For robot safety, we would like it to respect some boundaries. For instance, learning not to cross some angular red lines.
  Stall torque costs could also benefit in getting more energy-efficient and stable agent.
  Angular displacement cost, could discipline the legs.

## Slide 7: Reward Shaping: Types of issues
You really need to recognize the type of issue.
Each has its own cures. You should not confuse the two.
You may end up alternating between the two.
Policy Optimization problems
Unwanted semi-optimal agent behaviors

## Slide 8: Standing video

## Slide 9: Obstacle avoidance

## Slide 10: Obstacle avoidance

## Slide 11: Future Work
Hardware implementation of the Simulation-Learned policy
  Making sure that the controller would not harm the device
Hardware online learning
  Reducing sample complexity

## Slide 12: References
Hae-Won Park, Patrick M Wensing, and Sangbae Kim, “High-speed bounding with the MIT Cheetah 2: Control design and experiments,” The International Journal of Robotics Research, vol. 36, no. 2, Feb. 2017.
Schulman, J., Wolski, F., Dhariwal, P., Radford, A. and Klimov, O., 2017. Proximal policy optimization algorithms. arXiv preprint arXiv:1707.06347.

## Slide 13: Questions?

## Slide 14
Thank you