## Slide 1: Urban Path Planning to Minimize GPS Integrity Risk Using PPO
Sriramya “Ramya” Bhamidipati
Group Meeting 12/10/2018

## Slide 2: Motivation and Objectives
Multipath due to tall buildings in urban areas
Perform autonomous path planning to minimize the GPS integrity risk, induced due to multipath
Start point
End point
Multiple possible routes
Blocked
Non-line of Sight
Line of Sight
[D. Chen]

## Slide 3: Aspects and Assumptions
Assumptions:
  GPS satellites are considered static and clock bias errors are ignored
  Buildings are considered rectangle blocks and uniform distributions with heights ranging from 20-100m
Given the grid layout of roads in urban areas,
  Discrete control actions are considered
  Key decision making points are at intersections
  Along the rest of the street the same action is continued
Minimize the GPS integrity risk metric

## Slide 4: Simulated Environment
Multipath effects are induced due to the surrounding 4 buildings
Building models/LiDAR to obtain the 3D point cloud data
Constant goal is to reach the coordinates (800, 800, 4)
Blue are LOS GPS signals, red are the NLOS signals and dotted yellow are blocked by buildings

## Slide 5: Simulated Environment Cont’d.
Added multipath profiles to NLOS satellites to simulate tracking loop errors
  Tanh profile is considered based on random parameters for start time, rate, amplitude
SV 15, 25, 30: Direct Line of sight
SV 2, 3, 8, 13, 22: Non-line of sight
SV 21, 26: Blocked

## Slide 6: Reward
Three components:
  Integrity risk calculated via GPS RAIM-based solution separation Difference in distances between the previous and the current decision points
  On reaching the goal

## Slide 7: Actor-Critic: Discrete PPO
Separate NN designed for actor and critic
ReLu activation and categorical distribution for the actor
Actor consists of 3 linear hidden layers and critic consists of 4 layers, with 20 nodes in each layer

## Slide 8: Outline
Motivation and Prior Work
Algorithm Details
Results
  Case #1: Open-sky with 3D robot position as input
  Case #2: Urban area with 3D robot position as input
  Case #3: Open-sky with observations from GPS and 3D building models/LiDAR as input
  Case #4: Urban area with observations from GPS and 3D building models/LiDAR as input

## Slide 9: Case #1: Open Sky
Algorithms: Discrete PPO
Input: Current 3D position
Output: Discrete velocity
Heights of buildings are all 20m indicating relatively open-sky conditions
Deep RL-based discrete PPO accurately navigates the robot from arbitrary start position to GOAL

## Slide 10: Case #2: Urban Area Results
Input: Current 3D position
Output: Discrete velocity
Episode=100 steps
Heights range between 35-100m
Deep RL-based discrete PPO also converges, but Q-learning and SARSA perform slightly better

## Slide 11: Case #3 & #4: Architecture
RL-based Path Planning
pseudoranges
EKF Measurement Update
EKF Time Update
GPS antenna
Max height
3D building models/LiDAR
Control action: Velocity
Updated position
Predicted position
GOAL
Goal 3D position

## Slide 12: Case #3 & #4: Setup Details
Deep-RL Algorithm: Discrete PPO
Multi-core processing, number of workers = 8
Input to NN: []
  , is the height of building available at , i.e., based on max and min ranges, is pseudoranges from satellite, denote predicted position by EKF and goal position to be reached, (.) denotes measurement model
Output from NN: control velocity
  One of four discrete: forward, back, top or bottom

## Slide 13: Case #4: Training
Area: 0.25 sq km area with high-rise buildings
Light grey and black indicates height of 20m and 100m, respectively
Training time is ~6 hrs
Average time to goal=69.3s
Deep RL-based discrete PPO converges even when observation vector is used for training

## Slide 14: Case #4: Loss Function
Value loss of the critic quickly decreases whereas the clip loss of the actor gradually reduces

## Slide 15: Case #4: GPS Position Error
RMS GPS position error of path estimated via PPO is , the shortest path is
Start Point
Goal

## Slide 16: Future/Ongoing Work
Incorporate this to my research on SLAM-based integrity estimation
Analyze its performance for a larger urban areas
Utilize the trained policy in one urban section for navigating in another section
Satellites motion and the receiver clock bias errors
Arbitrary goal positions
Extending the work to generic urban area using
  Multiple actor and centralized critic to ensure that the robot learns both a local as well as a global policy

## Slide 17: Thank you
Sriramya Bhamidipati
Doctoral Student
University of Illinois at Urbana Champaign
Advisor: Prof. Grace Xingxin Gao
Email: sbhamid2@illinos .edu